## Slide 1: Transposition and Conversion
Lynn E. Lawrence, CPOT, COA, ABOC, OSC

## Slide 2: Answers on presentation
Some of the answers in this presentation are intentionally incorrect, so be prepared to defend your answers…

## Slide 3: Purpose
Why is the math necessary?
When is the math going to be used?
Does this alter the patients SRx

## Slide 4: Create a number line
10 9 8 7 6 5 4 3 2 1 0 1 2 3 4 5 6 7 8 9 10
Insert 3 hash marks between every number
111
111
111
111
111
111
111
111
111
111
111
111
111
111
111
111
111
111
111
111
111

## Slide 5: Determining cylinder power
Two questions should be asked to determine the cylinder power:
1. In what direction on the number line is travel occurring (on the number line) from the sphere to the cylinder (either in the negative direction or in the positive direction)?
2. What is the distance traveled from the sphere to the cylinder power (the amount of cylinder present in the prescription)?

## Slide 6: Prescriptions: Transposition
Transposition
  Step 1 = Combine the sphere and cylinder power mathematically
  Step 2 = Change the sign of the cylinder
  Step 3 = Change the axis by 90 degrees
Hint: When combining positive and negative numbers, think in terms of money. Example: -2.00 combined with +0.50 If you are $2.00 “in the hole” and you deposit $0.50, what is your balance?
Answer: $1.50 “in the hole”, or -1.50.

## Slide 7: Transposition
Combine the sphere and cylinder power algebraically/mathematically
Keep and change the sign of the cylinder
Change the axis by 90 degrees
EX: +2.00+1.00 x 080
+3.00 -1.00 x 170
The purpose of transposition is to change the same prescription into a different form.

## Slide 8: Transposition 1 Minute Drill
Step 1 = Combine the sphere and cylinder power mathematically
Step 2 = Change the sign of the cylinder
Step 3 = Change the axis by 90 degrees
1. + 1.75 – 0.75 X 030
2. – 2.25 + 1.00 X 170
3. – 1.75 + 2.00 X 125

## Slide 9: Review Questions 1 minute drill
Transpose the following Rx from plus cylinder form to minus cylinder form
-2.00 +1.00 x 090
Answer ______________
-1.00 +3.00 x 070
Answer ______________
-1.00 +1.50 x 010
Answer______________
- 0.50 +2.00 x 145
Answer______________
-3.00 +2.00 x 095
Answer______________

## Slide 10: Transposition 1 Minute Drill
Step 1 = Combine the sphere and cylinder power mathematically
Step 2 = Change the sign of the cylinder
Step 3 = Change the axis by 90 degrees
1. + 1.75 – 0.75 X 030
2. – 2.25 + 1.00 X 170
3. – 1.75 + 2.00 X 125

## Slide 11: Review Questions 1 minute drill
Convert the following prescription from minus cylinder to plus cylinder format
-1.00 -1.00 x 090
Answer______________
- 0.50 -2.00 x 008
Answer______________
-1.00 -1.50 x 160
Answer______________
- 5.00 -3.00 x 088
Answer______________
-3.00 -1.50 x 095
Answer______________

## Slide 12: Review Questions 3 minutes
-2.00 -1.00 x 002 transpose
Answer______________
- 3.50 -2.00 x 080 transpose
Answer______________
-3.00 -2.50 x 016 transpose
Answer______________
- 3.00 -2.00 x 088 transpose
Answer______________
-2.00 -2.50 x 005 transpose
Answer______________
- 2.50 + 1.50 x 103 transpose
Answer______________
-1.00 + 0.50 x 162 transpose
Answer______________
+ 2.50 + 2.50 x 103 transpose
Answer______________
-2.50 + 1.00 x 029 transpose
Answer______________

## Slide 13: Spherical Equivalent
- Take half the cylinder and add algebraically to sphere
- Drop the cylinder and axis and write sphere only
EX. -2.00 -0.50 X 145
(half the cylinder) -0.25
(add to sphere) 0.25 + 2.00
Answer:
-2.25 Sph

## Slide 14: Convert to IV + NV Rx
Step 1
Take the ½ the add power and algebraically add it the sphere power of the Rx
Rewrite the Rx with ½ the add power remaining in Rx (used for reading)
* Used with computers or intermediate work
-2.50 – 1.25 x 125
- 1.50 – 1.00 x 095
Add +2.50
-4.50 – 2.50 x 005
- 1.50 – 1.00 x 150
Add +2.00

## Slide 15: Question
Transpose the following Rx to Near Vision Only aka NVO, SVN, reading glasses
-2.00 -1.00 x 080
-1.50 -2.00 x 180
+3.00 OU
Answer ___________________

## Slide 16: Question
Transpose the following Rx to Near Vision Only aka NVO, SVN, reading glasses
-1.00 – 0.50 x 010
-2.00 -0.75 x 100
+1.50 OU
Answer____________________

## Slide 17: Question
Transpose the following Rx to Near Vision Only aka NVO, SVN, reading glasses
-4.00 -0.25 x 090
-1.00 -0.50 x 098
+2.00 OU
Answer ___________________

## Slide 18: Question
Transpose the following Rx to Near Vision Only aka NVO, SVN, reading glasses
+2.50 -1.00 x 090
+1.00 -0.75 x 180
+2.50 OU
Answer ___________________

## Slide 19: Question
Convert to spherical equivalent
- 1.50 – 1.00 X 180
- 2.25 – 1.50 X 120
Answer____________________
+ 2.50 – 2.00 X 018
+ 2.25 – 3.50 X 010
Answer____________________

## Slide 20: Review Questions
Convert the following Rx to Near Vision Only aka NVO, SVN, reading glasses
-2.00 -1.00 x 080
-1.50 -2.00 x 180
+3.00 OU
Answer ________________
________________
-1.00 – 0.50 x 010
-2.00 -0.75 x 100
+1.25 OU
Answer________________
________________
-4.00 -0.25 x 090
-1.00 -0.50 x 098
+2.00 OU
Answer ________________
________________
+2.50 -1.00 x 090
+1.00 -0.75 x 180
+2.25 OU
Answer ________________
________________

## Slide 21: Review Questions 1 minute drill
Transpose the following Rx from plus cylinder form to minus cylinder form
-1.00 +1.00 x 040
Answer ______________
-2.00 +3.00 x 170
Answer ______________
-4.00 +1.50 x 100
Answer______________
- 1.50 +2.00 x 015
Answer______________
-3.00 +2.00 x 095
Answer______________

## Slide 22: Review Questions 1 minute drill
Convert the following prescription from minus cylinder to plus cylinder format
-1.00 -1.00 x 090
Answer______________
- 0.50 -2.00 x 008
Answer______________
-1.00 -1.50 x 160
Answer______________
- 5.00 -3.00 x 088
Answer______________
-3.00 -1.50 x 095
Answer______________

## Slide 23: Convert to SVN or Near Rx only 1 min drill
+ 3.25 – 0.75 X 125
+ 1.75 – 1.00 X 090
  Add 2.50
- 4.50 – 1.50 X 035
- 1.75 – 1.00 X 150
  Add 2.00
Step 1
  Add the add power to the sphere power and write it as the new sphere power
Step 2
  Write the new complete Rx Sph, Cyl, and Axis

## Slide 24: Review Questions
Convert the following Rx to Near Vision Only aka NVO, SVN, reading glasses
-2.00 -1.00 x 080
-1.50 -2.00 x 180
+3.00 OU
Answer ________________
________________
-1.00 – 0.50 x 010
-2.00 -0.75 x 100
+1.25 OU
Answer________________
________________
-4.00 -0.25 x 090
-1.00 -0.50 x 098
+2.00 OU
Answer ________________
________________
+2.50 -1.00 x 090
+1.00 -0.75 x 180
+2.25 OU
Answer ________________
________________

## Slide 25: martralyn@msn.com http://lynnslecturehelp.wordpress.com
Thank you very much